## Slide 1: CHARGE PUMPS FOR PLLs BY R. F. ADDO

## Slide 2: OUTLINE
Introduction
The Charge Pump
Basic Principle of Operation of a Conventional Charge Pump
Non-ideal Behavior
  Charge Sharing
  Charge Injection and Clock Feedthrough
  Current Mismatch
Charge pump architectures
  Type 1: Conventional Tristate
  Type 2: Current Steering Topology
  Type 3: Differential Input with Single – Ended Output Topology
  Type 4: Fully Differential Charge Pump Topology
  Type 5: High Voltage Charge Pumps
Design Considerations
Typical Charge Pump Designs
  Charge Pump Design 1: Dual Compensation Charge Pump
  Charge Pump Design 2: NMOS Topology for a Dual Compensation Charge Pump Implementation
  Charge Pump Design 3: Dual Compension Implementation of a PMOS – NMOS Charge Pump Topology
  Charge Pump Design 4: Low Voltage High Speed Charge Pump design
  Charge Pump Design 5: Charge Pump Design for Ultra Low Power PLL
  Charge Pump Design 6: Charge Pump Design for Low Phase Noise Low Power PLL
  Charge Pump Design 7: A Fully Differential Charge Pump
  Charge Pump Design 8: Charge Pump Design for a Low Power PLL
Summary
Reference

## Slide 3: Introduction
The figure below shows the block diagram of the various components in a typical charge pump PLL design
Block diagram of a typical PLL [14]

## Slide 4: OUTLINE
Introduction
The Charge Pump
Basic Principle of Operation of a Conventional Charge Pump
Non-ideal Behavior
  Charge Sharing
  Charge Injection and Clock Feedthrough
  Current Mismatch
Charge pump architectures
  Type 1: Conventional Tristate
  Type 2: Current Steering Topology
  Type 3: Differential Input with Single – Ended Output Topology
  Type 4: Fully Differential Charge Pump Topology
  Type 5: High Voltage Charge Pumps
Design Considerations
Typical Charge Pump Designs
  Charge Pump Design 1: Dual Compensation Charge Pump
  Charge Pump Design 2: NMOS Topology for a Dual Compensation Charge Pump Implementation
  Charge Pump Design 3: Dual Compension Implementation of a PMOS – NMOS Charge Pump Topology
  Charge Pump Design 4: Low Voltage High Speed Charge Pump design
  Charge Pump Design 5: Charge Pump Design for Ultra Low Power PLL
  Charge Pump Design 6: Charge Pump Design for Low Phase Noise Low Power PLL
  Charge Pump Design 7: A Fully Differential Charge Pump
  Charge Pump Design 8: Charge Pump Design for a Low Power PLL
Summary
Reference

## Slide 5: The Charge Pump
Charge pump is used to sink and source current into a loop – filter based on the output of a PFD
When the rising edge of the reference input REF leads that of the divided VCO feedback input, the PFD output up is high and the charge pump delivers charges to the capacitors in the loop filter. Thus, the loop filter output voltage increases and so do the VCO output frequency and phase.
The charge-pump transfers phase difference into current.
The charge-pump converts the up and dn pulses into current pulses and these current pulses change voltage drop on the loop filter impedance which is also the VCO control voltage.
Issues associated with charge pump are current mismatch, charge sharing, charge injection, noise and high power dissipation

## Slide 6: OUTLINE
Introduction
The Charge Pump
Basic Principle of Operation of a Conventional Charge Pump
Non-ideal Behavior
  Charge Sharing
  Charge Injection and Clock Feedthrough
  Current Mismatch
Charge pump architectures
  Type 1: Conventional Tristate
  Type 2: Current Steering Topology
  Type 3: Differential Input with Single – Ended Output Topology
  Type 4: Fully Differential Charge Pump Topology
  Type 5: High Voltage Charge Pumps
Design Considerations
Typical Charge Pump Designs
  Charge Pump Design 1: Dual Compensation Charge Pump
  Charge Pump Design 2: NMOS Topology for a Dual Compensation Charge Pump Implementation
  Charge Pump Design 3: Dual Compension Implementation of a PMOS – NMOS Charge Pump Topology
  Charge Pump Design 4: Low Voltage High Speed Charge Pump design
  Charge Pump Design 5: Charge Pump Design for Ultra Low Power PLL
  Charge Pump Design 6: Charge Pump Design for Low Phase Noise Low Power PLL
  Charge Pump Design 7: A Fully Differential Charge Pump
  Charge Pump Design 8: Charge Pump Design for a Low Power PLL
Summary
Reference

## Slide 7: Basic Principle of Operation of a Conventional Charge Pump
UP state: the switch SM1 is on and SM2 is off; the load
capacitor CL is charged by Iup and the voltage Vc rises.
DOWN state: SM1 is off and SM2 is on, which causes
CL to be discharged by Idn and Vc falls.
HOLD state: SM1 and SM2 are both off, then no current
flows into CL and Vc is held, which means that the PLL
is locked. In ideal case, SM1 and SM2 will never be on at
the same time.
SM1 and SM2 are usually implemented using PMOS and
NMOS devices respectively
[5]
Fig 1. Schematic of conventional charge pump [5]

## Slide 8: OUTLINE
Introduction
The Charge Pump
Basic Principle of Operation of a Conventional Charge Pump
Non-ideal Behavior
  Charge Sharing
  Charge Injection and Clock Feedthrough
  Current Mismatch
Charge pump architectures
  Type 1: Conventional Tristate
  Type 2: Current Steering Topology
  Type 3: Differential Input with Single – Ended Output Topology
  Type 4: Fully Differential Charge Pump Topology
  Type 5: High Voltage Charge Pumps
Design Considerations
Typical Charge Pump Designs
  Charge Pump Design 1: Dual Compensation Charge Pump
  Charge Pump Design 2: NMOS Topology for a Dual Compensation Charge Pump Implementation
  Charge Pump Design 3: Dual Compension Implementation of a PMOS – NMOS Charge Pump Topology
  Charge Pump Design 4: Low Voltage High Speed Charge Pump design
  Charge Pump Design 5: Charge Pump Design for Ultra Low Power PLL
  Charge Pump Design 6: Charge Pump Design for Low Phase Noise Low Power PLL
  Charge Pump Design 7: A Fully Differential Charge Pump
  Charge Pump Design 8: Charge Pump Design for a Low Power PLL
Summary
Reference

## Slide 9: Non-ideal Behavior: Charge Sharing
There will be charge sharing which is mostly caused by
the positions of the two switch transistors.
When SM1 and SM2 are both off, the voltage at the node X,
Vx is pulled up to Vdd, the voltage at the node Y, Vy is
pulled down to Gnd and the Vc is floating.
For the non-ideal narrow pulses in the signal UP, there is a
series of short period when the two switches are both on
simultaneously.
This will cause the Vx to decrease and Vy to increase, which
will result in a consequent deviation in the output Vc due to
the charge sharing between CL and Cx, Cy as shown in the
curve (II) in Fig 3 (b).
A conventional solution is to use a unity gain amplifier to
keep the Vx and Vy at the same level equal to Vc when the
switch SM1 and SM2 are both on.
[5]
Fig 2. Schematic of conventional charge pump with a unity gain amplifier [5]
Fig. 3. Output waveforms, (a) ideal and (b) various non-ideal case [5].

## Slide 10: OUTLINE
Introduction
The Charge Pump
Basic Principle of Operation of a Conventional Charge Pump
Non-ideal Behavior
  Charge Sharing
  Charge Injection and Clock Feedthrough
  Current Mismatch
Charge pump architectures
  Type 1: Conventional Tristate
  Type 2: Current Steering Topology
  Type 3: Differential Input with Single – Ended Output Topology
  Type 4: Fully Differential Charge Pump Topology
  Type 5: High Voltage Charge Pumps
Design Considerations
Typical Charge Pump Designs
  Charge Pump Design 1: Dual Compensation Charge Pump
  Charge Pump Design 2: NMOS Topology for a Dual Compensation Charge Pump Implementation
  Charge Pump Design 3: Dual Compension Implementation of a PMOS – NMOS Charge Pump Topology
  Charge Pump Design 4: Low Voltage High Speed Charge Pump design
  Charge Pump Design 5: Charge Pump Design for Ultra Low Power PLL
  Charge Pump Design 6: Charge Pump Design for Low Phase Noise Low Power PLL
  Charge Pump Design 7: A Fully Differential Charge Pump
  Charge Pump Design 8: Charge Pump Design for a Low Power PLL
Summary
Reference

## Slide 11: Non – Ideal Behavior: Charge Injection and Clock Feedthrough
Charge Injection
Charge injection is another consideration when designing a good CP.
When the current source/sink switches (eg. SM2) are on, there are charges under the gate of the transistor.
When the switch is turned off, the charge under the gate will be injected to the drain (node Vc) and the source (node Y) of the transistor.
If the switch is next to the output pin, the injected charge will cause ripple at the output as shown in curve III of fig 4d.
Clock Feedthrough
The clock feedthrough mechanism is due to the coupling capacitance from the
gate to both the source and drain of the CMOS device as shown in fig 4c.
When clock to NMOS goes high, the clock signal feeds through the gate/drain
and gate/source capacitors but because the NMOS is on, Vin is connected to CL
This charges CL to Vin so the clock feed through has no effect on Vout.
When the clock goes low, the NMOS is off. This creates a capacitive voltage
divider between the gate/drain and CL
As a result, a portion of the clock signal appears across CL
This will cause a ripple at the output if the switches are placed next to the
output terminal as shown in curve IV of fig 4d.
A solution involves placement of the switch away from the output node or to
place the switch at the source as shown in fig 4b. This will reduce the charge
injection and clock feedthrough effects.
Fig 4b. Placing the switch near the source to reduce the charge injection anf the clock feedthrough effects in a charge pump
Fig 4a. Schematic of conventional charge pump with a unity gain amplifier [5]
Fig. 4d. Output waveforms, various non-ideal cases [5].
Fig 4c. Clock Feedthrough
Vin
CL
Vout

## Slide 12: Non – Ideal Behavior: Charge Injection and Clock Feedthrough Reduction
DUMMY SWITCH
One of the way to reduce the clock feedthrough and the charge injection
by the use of a dummy switch as shown in fig 4e which is a MOS device
with its drain and source shorted and placed in series with the desired
switch M1 with its control signal being the inverted signal of that of M1.
When M1 turns off, half of the charge is injected into M2 which is half
the size of M1.
This charge injected by M1 is essentially matched by that induced by M2
hence overall charge injection is canceled.
When M2 turns off, it will inject half of its charge in both directions but
since the drain and the source are shorted and M1 is on, all the charge
charge from M2 will be injected onto the low – impedance voltage driven
source which is charging CL
Therefore this charge will not affect the value of the voltage on CL
TRANSMISSION GATE
A 2nd approach is to replace the switch with a transmission gate
This will result in lower changes in Vout because the complementary signal used will act to cancel each other out however a precise control of the complementary signals used is required (i.e. they must be switched exactly at the same time)
M1
M2
Fig 4e. Using dummy switch to reduce the charge injection and the clock feedthrough effects in a charge pump

## Slide 13: OUTLINE
Introduction
The Charge Pump
Basic Principle of Operation of a Conventional Charge Pump
Non-ideal Behavior
  Charge Sharing
  Charge Injection and Clock Feedthrough
  Current Mismatch
Charge pump architectures
  Type 1: Conventional Tristate
  Type 2: Current Steering Topology
  Type 3: Differential Input with Single – Ended Output Topology
  Type 4: Fully Differential Charge Pump Topology
  Type 5: High Voltage Charge Pumps
Design Considerations
Typical Charge Pump Designs
  Charge Pump Design 1: Dual Compensation Charge Pump
  Charge Pump Design 2: NMOS Topology for a Dual Compensation Charge Pump Implementation
  Charge Pump Design 3: Dual Compension Implementation of a PMOS – NMOS Charge Pump Topology
  Charge Pump Design 4: Low Voltage High Speed Charge Pump design
  Charge Pump Design 5: Charge Pump Design for Ultra Low Power PLL
  Charge Pump Design 6: Charge Pump Design for Low Phase Noise Low Power PLL
  Charge Pump Design 7: A Fully Differential Charge Pump
  Charge Pump Design 8: Charge Pump Design for a Low Power PLL
Summary
Reference

## Slide 14: Non – Ideal Behavior: Current Mismatch
If the current values lup and Idn are not exactly same, or there is some delay between the controlled signals UP and DN, then there will be a natural phase error between reference frequency and output frequency of the VCO even if the PLL is in locked state.
The reason is that the voltage Vc must be constant when the PLL is locked. In other words the quantity of charge Qcharge and the one of discharge Qdischarge at the load CL must be equal at the time
Qcharge = lup x tup = Qdischarge = ldn x tdn
where tup and tdn are the charging and discharging times in one cycle
If the values of lup and Idn, are different, then there has to be a constant difference of switch-on time Δt between SM1 and SM2 at every comparing cycle, which means a relevant phase difference Δɵo exists at the two inputs of P/FD, as illustrated in Fig. 5.
Specifically, the phase difference Δɵo between reference frequency and the output frequency of the VCO will always exists, even when the whole loop is in a locked state.
[5]
Fig. 5. Mismatch issue in charge pump circuits.[5]

## Slide 15: Non – Ideal Behavior: Current Mismatch (cont.)
  The classical method of reducing the current mismatch of the charge pump is to either increase the output resistance of the pump or to use a compensation method
  The output resistance of the charge pump can be increased by either using a cascode or a gain – boosting topology. This will however reduce the output dynamic range and prevent the use of the pump for low voltage operations.
  The compensation method is implemented by the use of operational amplifier.
  The op – amp enables the pump currents to track each other and then compensate for any mismatch.
  This will however result in higher power consumption and an area overhead due to the addition of the op – amp
  Other sources of current mismatch are process variation and charge sharing [6].
CONVENTIONAL CHARGE PUMP
Fig 6a shows a conventional charge pump
schematic and fig 6b shows the current
matching characteristics
When the VCP is equal to the biasing
voltage VR of the PMOS, the pump – up
current IUP is equal to the pump – down
current IDN
When the the VCP deviates from the VR,
the difference between the pumping –
up and the pumping – down current
increases due to channel length
modulation effect. [2]
[2]
Fig 6a. Schematic of conventional charge pump
Fig 6b. Current matching characteristics the of conventional charge pump

## Slide 16: Non – Ideal Behavior: Current Mismatch Minimization (cont.)
CASCODE METHOD
Fig 7a shows a schematic of a conventional
cascode charge pump and fig 7b shows its
current matching characteristics
In the cascode CP, more cascode devices must
be stacked to increase the output resistance.
By increasing the output resistance, current
mismatch can be reduced.
However, stacked cascode devices reduce the
output dynamic range.
COMPENSATION METHOD
This uses an op – amp to implement a
negative feedback loop which controls
the PMOS bias voltage VR so that it
matches the output voltage VCP
This reduces the difference in current
which causes the pump – up current and
the pump – down current to be equal.
But there still exist a current variation
with the VCP. [2], [3]
Fig 7a. Schematic of conventional cascode charge pump [2]
Fig 7b. Current matching characteristics the of conventional cascode CP [2]
Fig 7c. Schematic of conventional compensated charge pump [2]
Fig 7d. Current matching characteristics the of compensated CP [2]

## Slide 17: OUTLINE
Introduction
The Charge Pump
Basic Principle of Operation of a Conventional Charge Pump
Non-ideal Behavior
  Charge Sharing
  Charge Injection and Clock Feedthrough
  Current Mismatch
Charge pump architectures
  Type 1: Conventional Tristate
  Type 2: Current Steering Topology
  Type 3: Differential Input with Single – Ended Output Topology
  Type 4: Fully Differential Charge Pump Topology
  Type 5: High Voltage Charge Pumps
Design Considerations
Typical Charge Pump Designs
  Charge Pump Design 1: Dual Compensation Charge Pump
  Charge Pump Design 2: NMOS Topology for a Dual Compensation Charge Pump Implementation
  Charge Pump Design 3: Dual Compension Implementation of a PMOS – NMOS Charge Pump Topology
  Charge Pump Design 4: Low Voltage High Speed Charge Pump design
  Charge Pump Design 5: Charge Pump Design for Ultra Low Power PLL
  Charge Pump Design 6: Charge Pump Design for Low Phase Noise Low Power PLL
  Charge Pump Design 7: A Fully Differential Charge Pump
  Charge Pump Design 8: Charge Pump Design for a Low Power PLL
Summary
Reference

## Slide 18: Charge pump architectures: Type 1: Conventional Tristate [1]
This is also called the single – ended charge pump.
It has a lower current consumption depending on the frequency of the PFD
There are three topologies for this type of charge pump: the switch – in – drain, switch – in- gate and switch – in – source.
Switch – in – Drain
This charge pump has its switch at the drain of the
current mirror device
When the switch DW is turned off, the current pulls the
drain of M1to ground. After the switch is turned on,
the voltage at the drain of M1 increases from 0V to
the loop filter voltage held by PLL.
In the mean time, M1 has to be in the linear region
till the voltage at the drain of MI is higher than the
minimum saturation voltage.
During this time, high peak current is generated
due to voltage difference of two series turn-on
resistors from the current mirror, M1, and the switch.
On the PMOS side, the same situation will occur and
the matching of this peak current is difficult since the
amount of the peak current varies with the output
voltage.
It also has a high charge sharing between the node at
drain of M1 and M2 and the loop filter when the switch
is turned on.
[1]
Fig 8. Schematic of conventional switch – in – drain single – ended charge pump [1]

## Slide 19: Charge pump architectures: Type 1: Conventional Tristate [1] (cont.)
Switch – in – Gate
This type has its switch at the gate instead of the drain.
With this topology, the current mirrors are guaranteed
to be in the saturation region.
To achieve fast switching time, however, the bias current
of M3 and M4 may not be scaled down since the gm3,4
affects the switching time constant in this configuration.
The gate capacitance of M1 and M2 is substantial when
the output current of the charge pump is high.
long channel devices is used for better current matching
this will lead to a large parasitic capacitance which will
cause the charge sharing, charge injection and clock
feedthrough to be high
Fig 9. Schematic of conventional switch – in – gate single – ended charge pump [1]

## Slide 20: Charge pump architectures: Type 1: Conventional Tristate [1] (cont.)
Switch – in – Source
The switch can also be located at the source of the
current mirror device
M1 and M2 are in the saturation all the time.
The gm3,4 does not affect the switching time as it
did in the switch – in – gate type.
As a result, the low bias current can be used with
high output current.
This architecture gives faster switching time than the
gate switching since the switch is connected to single
transistor with lower parasitic capacitance.
It is also relatively simple to implement and has low
power consumption
Improving the Performance of This Type of Charge Pump
A unity gain amplifier could be included in the tristate
charge pump topology to help in the reduction of
charge sharing
With the unity gain amplifier, the voltage at the drain of
M1 and M2 is set to the voltage at the output node when
the switch is off thereby reducing the charge sharing
effect when the switch is turned on.
This architecture is useful when the parasitic capacitance
is comparable to the value of the capacitor in the loop filter.
Fig 10. Schematic of conventional switch – in – source single – ended charge pump [1]
Fig 11. using unity gain amplifier to improve the performance of the single – ended charge pump [1]

## Slide 21: OUTLINE
Introduction
The Charge Pump
Basic Principle of Operation of a Conventional Charge Pump
Non-ideal Behavior
  Charge Sharing
  Charge Injection and Clock Feedthrough
  Current Mismatch
Charge pump architectures
  Type 1: Conventional Tristate
  Type 2: Current Steering Topology
  Type 3: Differential Input with Single – Ended Output Topology
  Type 4: Fully Differential Charge Pump Topology
  Type 5: High Voltage Charge Pumps
Design Considerations
Typical Charge Pump Designs
  Charge Pump Design 1: Dual Compensation Charge Pump
  Charge Pump Design 2: NMOS Topology for a Dual Compensation Charge Pump Implementation
  Charge Pump Design 3: Dual Compension Implementation of a PMOS – NMOS Charge Pump Topology
  Charge Pump Design 4: Low Voltage High Speed Charge Pump design
  Charge Pump Design 5: Charge Pump Design for Ultra Low Power PLL
  Charge Pump Design 6: Charge Pump Design for Low Phase Noise Low Power PLL
  Charge Pump Design 7: A Fully Differential Charge Pump
  Charge Pump Design 8: Charge Pump Design for a Low Power PLL
Summary
Reference

## Slide 22: Charge pump architectures [1]
Type 2: Current Steering Topology
charge pump with the current steering switch
as shown in Fig. 12.
The performance is similar to the single – ended
topology however the switching time is greatly
improved due to current switch.
The disadvantage of this topology is that it has
high static power consumption
Type 3: Differential Input with Single – Ended Output Topology
This type is also called the NMOS charge pump topology
It uses NMOS devices to implement the switches for the UP
and DOWN signals
This helps in the reduction of current mismatch which
usually exist due to the mismatch between the PMOS device
used to implement the UP switch and the NMOS device used
for the DOWN switch.
This topology has medium current consumption and moderate
performance
Fig 12. Schematic of a current steering charge pump topology [1]
Fig 13. Schematic of a differential input single – ended output topology [1]

## Slide 23: OUTLINE
Introduction
The Charge Pump
Basic Principle of Operation of a Conventional Charge Pump
Non-ideal Behavior
  Charge Sharing
  Charge Injection and Clock Feedthrough
  Current Mismatch
Charge pump architectures
  Type 1: Conventional Tristate
  Type 2: Current Steering Topology
  Type 3: Differential Input with Single – Ended Output Topology
  Type 4: Fully Differential Charge Pump Topology
  Type 5: High Voltage Charge Pumps
Design Considerations
Typical Charge Pump Designs
  Charge Pump Design 1: Dual Compensation Charge Pump
  Charge Pump Design 2: NMOS Topology for a Dual Compensation Charge Pump Implementation
  Charge Pump Design 3: Dual Compension Implementation of a PMOS – NMOS Charge Pump Topology
  Charge Pump Design 4: Low Voltage High Speed Charge Pump design
  Charge Pump Design 5: Charge Pump Design for Ultra Low Power PLL
  Charge Pump Design 6: Charge Pump Design for Low Phase Noise Low Power PLL
  Charge Pump Design 7: A Fully Differential Charge Pump
  Charge Pump Design 8: Charge Pump Design for a Low Power PLL
Summary
Reference

## Slide 24: Charge pump architectures: Type 4: Fully Differential Charge Pump Topology [1], [7]
A typical fully differential charge pump
topology is as shown in fig. 13
It has several advantages over the single –
ended topology [1]
These includes
  Firstly, the switch mismatches between
  NMOS transistors and PMOS transistors
  does not substantially affect the overall
  performance.
  Secondly, the differential charge pump
  has switches using only NMOS transistors
  which also helps with the reduction of the
  current mismatch.
  Thirdly, this configuration doubles the
  range of the output voltage compliance
  compared to the single-ended charge
  pump. For low-voltage operation, the
  limited output voltage range of the single – ended charge pump makes it difficult for the VCO to meet the specified tuning range unless the VCO gain is increased.
  Fourthly, the differential output stage is less sensitive to leakage current since the leakage current
behaves as a common-mode offset with the dual output stages. ???
  Lastly, the differential charge pump with two loop filters provides better immunity to the supply, ground and the substrate noise when on-chip loop filters are used.
  However, these advantages can be achieved at the cost of two loop filters, common-mode feedback circuitry and more power dissipation due to the constant current biasing.
Fig 13. Schematic of a typical fully differential charge pump topology [7]

## Slide 25: OUTLINE
Introduction
The Charge Pump
Basic Principle of Operation of a Conventional Charge Pump
Non-ideal Behavior
  Charge Sharing
  Charge Injection and Clock Feedthrough
  Current Mismatch
Charge pump architectures
  Type 1: Conventional Tristate
  Type 2: Current Steering Topology
  Type 3: Differential Input with Single – Ended Output Topology
  Type 4: Fully Differential Charge Pump Topology
  Type 5: High Voltage Charge Pumps
Design Considerations
Typical Charge Pump Designs
  Charge Pump Design 1: Dual Compensation Charge Pump
  Charge Pump Design 2: NMOS Topology for a Dual Compensation Charge Pump Implementation
  Charge Pump Design 3: Dual Compension Implementation of a PMOS – NMOS Charge Pump Topology
  Charge Pump Design 4: Low Voltage High Speed Charge Pump design
  Charge Pump Design 5: Charge Pump Design for Ultra Low Power PLL
  Charge Pump Design 6: Charge Pump Design for Low Phase Noise Low Power PLL
  Charge Pump Design 7: A Fully Differential Charge Pump
  Charge Pump Design 8: Charge Pump Design for a Low Power PLL
Summary
Reference

## Slide 26: Charge pump architectures: Type 5: High Voltage Charge Pumps [8]
This type of charge pump gives very high output voltages higher than the supply voltage
In many applications such as the Power IC, continuous time filters, EEPROMs, and switched-capacitor transformers, automotive parts, telecom interfaces, cellular phones and microelectromechanical systems (MEMS), voltages higher than the power supplies are frequently required. [8], [9]
Increased voltage levels are obtained in a charge pump as a result of transferring charges to a capacitive load, and do not involve amplifiers or regular transformers.
The operating supply voltage for high voltage (HV) applications is increasing steadily, ranging from 20V to 300V.
They can be grouped into the following topologies:
The Voltage Doubler Cascade Charge Pump
This type includes: two-phase voltage doubler (TPVD), the Makowski charge pump and the multi-phase voltage doubler (MPVD).
These circuits generally have the best output ripple on the market
Difficult to implement for higher number of stages (> 10 stages)
Dickson Charge Pump [9]
Dickson charge pump exhibits a linear growth of the number of devices used with the voltage gain level, while the voltage doublers and Makowski charge pumps requirements for the devices grow
logarithmically with the voltage gain
The Pelliconi Cascade Charge Pump
It’s gain is higher than the gain of any other additive architecture
Its uses simple clocking (uses simple 2-phase non-overlapping clock generator).
Also, its output ripples is comparable to the ripple produced by voltage doublers.
This also exhibits a linear growth in the number of stages, however, since the voltage gain for the Pelliconi architecture is 2.6 times higher than the gain of a Dickson charge pump, and almost twice that of a single cascade charge pump, the number of stages needed to reach a specific output voltage is reduced.

## Slide 27: OUTLINE
Introduction
The Charge Pump
Basic Principle of Operation of a Conventional Charge Pump
Non-ideal Behavior
  Charge Sharing
  Charge Injection and Clock Feedthrough
  Current Mismatch
Charge pump architectures
  Type 1: Conventional Tristate
  Type 2: Current Steering Topology
  Type 3: Differential Input with Single – Ended Output Topology
  Type 4: Fully Differential Charge Pump Topology
  Type 5: High Voltage Charge Pumps
Design Considerations
Typical Charge Pump Designs
  Charge Pump Design 1: Dual Compensation Charge Pump
  Charge Pump Design 2: NMOS Topology for a Dual Compensation Charge Pump Implementation
  Charge Pump Design 3: Dual Compension Implementation of a PMOS – NMOS Charge Pump Topology
  Charge Pump Design 4: Low Voltage High Speed Charge Pump design
  Charge Pump Design 5: Charge Pump Design for Ultra Low Power PLL
  Charge Pump Design 6: Charge Pump Design for Low Phase Noise Low Power PLL
  Charge Pump Design 7: A Fully Differential Charge Pump
  Charge Pump Design 8: Charge Pump Design for a Low Power PLL
Summary
Reference

## Slide 28: Design Considerations For PLL’s Charge Pump
The necessary requirements for designing an effective charge pump circuit are:
  Avoid the charge sharing;
  Minimize the effect caused by charge injection and clock feed-through phenomena
  Match the current values of Iup and Idn and make sure that there is no time mismatch between UP and DN.
  Low power consumption

## Slide 29: OUTLINE
Introduction
The Charge Pump
Basic Principle of Operation of a Conventional Charge Pump
Non-ideal Behavior
  Charge Sharing
  Charge Injection and Clock Feedthrough
  Current Mismatch
Charge pump architectures
  Type 1: Conventional Tristate
  Type 2: Current Steering Topology
  Type 3: Differential Input with Single – Ended Output Topology
  Type 4: Fully Differential Charge Pump Topology
  Type 5: High Voltage Charge Pumps
Design Considerations
Typical Charge Pump Designs
  Charge Pump Design 1: Dual Compensation Charge Pump
  Charge Pump Design 2: NMOS Topology for a Dual Compensation Charge Pump Implementation
  Charge Pump Design 3: Dual Compension Implementation of a PMOS – NMOS Charge Pump Topology
  Charge Pump Design 4: Low Voltage High Speed Charge Pump design
  Charge Pump Design 5: Charge Pump Design for Ultra Low Power PLL
  Charge Pump Design 6: Charge Pump Design for Low Phase Noise Low Power PLL
  Charge Pump Design 7: A Fully Differential Charge Pump
  Charge Pump Design 8: Charge Pump Design for a Low Power PLL
Summary
Reference

## Slide 30: CHARGE PUMP DESIGN 1 [2]
This paper focuses on the reduction of the
current mismatch of the charge pump
This uses a dual compensation method which
uses two feedback loops to keep track of the
voltage difference to reduce both the current
mismatch and the current variation of the
pumping – up and pumping – down current.
In the first feedback loop, VR1 is controlled
to track VCP by a compensation method. So
the pump-up current (IUP) is equal to the bias
current (IB).
In the second feedback loop, VR2 is
controlled to track VCP so that the pump-down
current (IDN) is equal to the pump-up
current (IUP).
Results:
SIMULATED
Current mismatch = 0.15%
Current deviation = 1.42%
MEASURED:
Current mismatch = 1.4%
Current deviation = 3.8%
Fig 14a. Schematic of dual compensation charge pump [2]
Fig 14b. Simulation result of the circuit. (a) Current matching characteristics. (b) Difference between pump-up and pump-down current. [2]
(a)
(b)

## Slide 31: OUTLINE
Introduction
The Charge Pump
Basic Principle of Operation of a Conventional Charge Pump
Non-ideal Behavior
  Charge Sharing
  Charge Injection and Clock Feedthrough
  Current Mismatch
Charge pump architectures
  Type 1: Conventional Tristate
  Type 2: Current Steering Topology
  Type 3: Differential Input with Single – Ended Output Topology
  Type 4: Fully Differential Charge Pump Topology
  Type 5: High Voltage Charge Pumps
Design Considerations
Typical Charge Pump Designs
  Charge Pump Design 1: Dual Compensation Charge Pump
  Charge Pump Design 2: NMOS Topology for a Dual Compensation Charge Pump Implementation
  Charge Pump Design 3: Dual Compension Implementation of a PMOS – NMOS Charge Pump Topology
  Charge Pump Design 4: Low Voltage High Speed Charge Pump design
  Charge Pump Design 5: Charge Pump Design for Ultra Low Power PLL
  Charge Pump Design 6: Charge Pump Design for Low Phase Noise Low Power PLL
  Charge Pump Design 7: A Fully Differential Charge Pump
  Charge Pump Design 8: Charge Pump Design for a Low Power PLL
Summary
Reference

## Slide 32: CHARGE PUMP DESIGN 2 [4]
This uses the NMOS charge pump topology
to implement a dual compensation charge
pump to reduce the effect of channel
modulation and hence current mismatch
It uses two differential amplifiers which uses
PMOS as it input device in one and an NMOS
as the input device of the other.
When the UP signal is active, the differential
amplifier with the NMOS input pairs is used
regulate the VDSP4 at Vbn which is fixed at 1.5V.
This helps in increasing the output range.
When the DN signal is active, the differential
amplifier with the PMOS input pair is used to
regulate VDSN9 at Vbp which is fixed at 0.3V.
this also helps in increasing the output range
Result
Maximum current variation < 1%
[4]
Fig 15. Schematic of design

## Slide 33
[4]
Fig 16a. Schematic of the differential amplifier with NMOS input devices
Fig 16b. Schematic of the differential amplifier with PMOS input devices
Fig 16c. Current matching characteristic of a charge pump without compensation
Fig 16d. Current matching characteristic of this design

## Slide 34: OUTLINE
Introduction
The Charge Pump
Basic Principle of Operation of a Conventional Charge Pump
Non-ideal Behavior
  Charge Sharing
  Charge Injection and Clock Feedthrough
  Current Mismatch
Charge pump architectures
  Type 1: Conventional Tristate
  Type 2: Current Steering Topology
  Type 3: Differential Input with Single – Ended Output Topology
  Type 4: Fully Differential Charge Pump Topology
  Type 5: High Voltage Charge Pumps
Design Considerations
Typical Charge Pump Designs
  Charge Pump Design 1: Dual Compensation Charge Pump
  Charge Pump Design 2: NMOS Topology for a Dual Compensation Charge Pump Implementation
  Charge Pump Design 3: Dual Compension Implementation of a PMOS – NMOS Charge Pump Topology
  Charge Pump Design 4: Low Voltage High Speed Charge Pump design
  Charge Pump Design 5: Charge Pump Design for Ultra Low Power PLL
  Charge Pump Design 6: Charge Pump Design for Low Phase Noise Low Power PLL
  Charge Pump Design 7: A Fully Differential Charge Pump
  Charge Pump Design 8: Charge Pump Design for a Low Power PLL
Summary
Reference

## Slide 35: CHARGE PUMP DESIGN 3 [3]
This uses two compensation circuit to help in the
reduction of the current mismatch and current variation.
The circuit has two push-pull charge pumps (CP1 and
CP2) and two replica-feedback biasing circuits
(compensator 1 and 2).
The ﬁrst compensator controls the bias voltage VBP2 so
that the charging current of the CP2 (ICH2) can be kept
equal to the discharging current of the CP1 (IDIS1).
The second compensator controls VBN2 so that the
discharging current of the CP2 (IDIS2) can be kept equal
to the charging current of the CP1 (ICH1).
As a result, the total charging and discharging currents
are kept the same.
[3]
Fig 17. Schematic of design
Fig 18. Simulated output currents of (a) Conventional charge pump (b )Proposed charge pump
 | Maximum Current Mismatch | Maximum Current Variation
Conventional charge pump | 30.10% | 20.60%
Proposed charge pump | 3.20% | 1.70%

## Slide 36: OUTLINE
Introduction
The Charge Pump
Basic Principle of Operation of a Conventional Charge Pump
Non-ideal Behavior
  Charge Sharing
  Charge Injection and Clock Feedthrough
  Current Mismatch
Charge pump architectures
  Type 1: Conventional Tristate
  Type 2: Current Steering Topology
  Type 3: Differential Input with Single – Ended Output Topology
  Type 4: Fully Differential Charge Pump Topology
  Type 5: High Voltage Charge Pumps
Design Considerations
Typical Charge Pump Designs
  Charge Pump Design 1: Dual Compensation Charge Pump
  Charge Pump Design 2: NMOS Topology for a Dual Compensation Charge Pump Implementation
  Charge Pump Design 3: Dual Compension Implementation of a PMOS – NMOS Charge Pump Topology
  Charge Pump Design 4: Low Voltage High Speed Charge Pump design
  Charge Pump Design 5: Charge Pump Design for Ultra Low Power PLL
  Charge Pump Design 6: Charge Pump Design for Low Phase Noise Low Power PLL
  Charge Pump Design 7: A Fully Differential Charge Pump
  Charge Pump Design 8: Charge Pump Design for a Low Power PLL
Summary
Reference

## Slide 37: CHARGE PUMP DESIGN 4 [5]
In this paper, a novel charge pump circuit is proposed,
which is suitable for very high speed and low voltage
applications.
The pull-down part of the charge pump
circuit is described in Fig. 19. For the pull-up part, a
similar complementary circuit is used.
the charging current Iup and the discharging
current Idn are both derived from the same reference
current source IBIAS via the current mirrors containing
the transistors M1- M7.
M8, which does not directly connect with the output load
Helps in the reduction of the negative effect of the charge
sharing due to the position of the switch transistor.
When DOWN is equal to Gnd, there is no current
flowing through M11 and M12.
The voltage at the node A, VA is held at zero; When DOWN
switches to high level Vdd, M11 and M12 just act as a
voltage divider. Which causes the high level of VA to
depend on the (W/L) ratio of M11 to M12.
VA carefully chosen to cut off M10 when it is high. This will
cause the voltage at the node B, VB to be high due to the
transistor M9; if VA is zero, then VB will drop. The high and
low level of VB are relative to the (WIL) value of M9, M10
and even M8.
Power consumption = 28µW @ 1GHz for the PLL
Fig 19. Schematic of the pull – down part of the design
Fig 20. Waveform of the signal DOWN and VB

## Slide 38: OUTLINE
Introduction
The Charge Pump
Basic Principle of Operation of a Conventional Charge Pump
Non-ideal Behavior
  Charge Sharing
  Charge Injection and Clock Feedthrough
  Current Mismatch
Charge pump architectures
  Type 1: Conventional Tristate
  Type 2: Current Steering Topology
  Type 3: Differential Input with Single – Ended Output Topology
  Type 4: Fully Differential Charge Pump Topology
  Type 5: High Voltage Charge Pumps
Design Considerations
Typical Charge Pump Designs
  Charge Pump Design 1: Dual Compensation Charge Pump
  Charge Pump Design 2: NMOS Topology for a Dual Compensation Charge Pump Implementation
  Charge Pump Design 3: Dual Compension Implementation of a PMOS – NMOS Charge Pump Topology
  Charge Pump Design 4: Low Voltage High Speed Charge Pump design
  Charge Pump Design 5: Charge Pump Design for Ultra Low Power PLL
  Charge Pump Design 6: Charge Pump Design for Low Phase Noise Low Power PLL
  Charge Pump Design 7: A Fully Differential Charge Pump
  Charge Pump Design 8: Charge Pump Design for a Low Power PLL
Summary
Reference

## Slide 39: CHARGE PUMP DESIGN 5 [10]
This paper was interested in an ultra low power
PLL
The charge pump used in this paper is as shown
in fig 21.
The main metric of the charge pump in this paper
was a power.
Result
Technology: 0.13µm
Frequency : 600MHz
Supply voltage : 1.2V
Power : 53µW representing 26.5% of total power
Fig 21. Schematic of the charge pump for the design [10]

## Slide 40: OUTLINE
Introduction
The Charge Pump
Basic Principle of Operation of a Conventional Charge Pump
Non-ideal Behavior
  Charge Sharing
  Charge Injection and Clock Feedthrough
  Current Mismatch
Charge pump architectures
  Type 1: Conventional Tristate
  Type 2: Current Steering Topology
  Type 3: Differential Input with Single – Ended Output Topology
  Type 4: Fully Differential Charge Pump Topology
  Type 5: High Voltage Charge Pumps
Design Considerations
Typical Charge Pump Designs
  Charge Pump Design 1: Dual Compensation Charge Pump
  Charge Pump Design 2: NMOS Topology for a Dual Compensation Charge Pump Implementation
  Charge Pump Design 3: Dual Compension Implementation of a PMOS – NMOS Charge Pump Topology
  Charge Pump Design 4: Low Voltage High Speed Charge Pump design
  Charge Pump Design 5: Charge Pump Design for Ultra Low Power PLL
  Charge Pump Design 6: Charge Pump Design for Low Phase Noise Low Power PLL
  Charge Pump Design 7: A Fully Differential Charge Pump
  Charge Pump Design 8: Charge Pump Design for a Low Power PLL
Summary
Reference

## Slide 41: CHARGE PUMP DESIGN 6 [11]
This paper was interested in designing a low phase
noise low power PLL using low operating voltages
The proposed charge pump is as shown in Fig. 22.
this uses a supply voltage of 0.8V
Power consumed by the PLL is 2.5mW
Power consumed by the LC VCO was 1.3mW (52%)
The rest of the blocks consumed the remaining
48% however the power breakdown for these other
blocks were not given
Fig 22. Schematic of the charge pump for the design [11]
Table 2. Summary of result

## Slide 42: OUTLINE
Introduction
The Charge Pump
Basic Principle of Operation of a Conventional Charge Pump
Non-ideal Behavior
  Charge Sharing
  Charge Injection and Clock Feedthrough
  Current Mismatch
Charge pump architectures
  Type 1: Conventional Tristate
  Type 2: Current Steering Topology
  Type 3: Differential Input with Single – Ended Output Topology
  Type 4: Fully Differential Charge Pump Topology
  Type 5: High Voltage Charge Pumps
Design Considerations
Typical Charge Pump Designs
  Charge Pump Design 1: Dual Compensation Charge Pump
  Charge Pump Design 2: NMOS Topology for a Dual Compensation Charge Pump Implementation
  Charge Pump Design 3: Dual Compension Implementation of a PMOS – NMOS Charge Pump Topology
  Charge Pump Design 4: Low Voltage High Speed Charge Pump design
  Charge Pump Design 5: Charge Pump Design for Ultra Low Power PLL
  Charge Pump Design 6: Charge Pump Design for Low Phase Noise Low Power PLL
  Charge Pump Design 7: A Fully Differential Charge Pump
  Charge Pump Design 8: Charge Pump Design for a Low Power PLL
Summary
Reference

## Slide 43: CHARGE PUMP DESIGN 7 [12]
In this paper, a fully differential charge pump is designed
The FDCP comprises a differential CP circuit, a control
signal generating circuit, and a CMFB circuit.
Fig. 23a shows the FDCP which consists of two differential
pairs, two replicas and a current bias.
Operational amplifiers A1 and A2 ensure equal voltages in
nodes OUTP and P, OUTN and N respectively making the
voltages at nodes A, B, C and D remain unchanged before
and after current switching.
The two replicas and amplifiers A3 and A4 are used to
minimize the current mismatch of the charge pump.
Resistors R1 and R2 as well as capacitors C1 and C2 are added
to filter out the high frequency noise of amplifiers A3 and A4.
The control signal of transistors M9–M16 were generated using
the circuit in fig 23b.
It consists of two buffers, two switching arrays, and two capacitors.
The operation principle of the CMFB circuit is that the output
common-mode voltage is detected and compared with a reference
voltage VCM.
The voltage difference is converted into an error current by a
transconductance amplifier (TA).
The error current is fed back into output nodes OUTP and OUTN
to adjust the common-mode voltage.
Result:
Power = 1.6mW
Reference spur = -69dBc
Fig 23a. Schematic of the fully differential charge pump for the design [12]
Fig 23b. Schematic of the control signal generating circuit [12]
Fig 23c. Schematic of the CMFB circuit [12]

## Slide 44: OUTLINE
Introduction
The Charge Pump
Basic Principle of Operation of a Conventional Charge Pump
Non-ideal Behavior
  Charge Sharing
  Charge Injection and Clock Feedthrough
  Current Mismatch
Charge pump architectures
  Type 1: Conventional Tristate
  Type 2: Current Steering Topology
  Type 3: Differential Input with Single – Ended Output Topology
  Type 4: Fully Differential Charge Pump Topology
  Type 5: High Voltage Charge Pumps
Design Considerations
Typical Charge Pump Designs
  Charge Pump Design 1: Dual Compensation Charge Pump
  Charge Pump Design 2: NMOS Topology for a Dual Compensation Charge Pump Implementation
  Charge Pump Design 3: Dual Compension Implementation of a PMOS – NMOS Charge Pump Topology
  Charge Pump Design 4: Low Voltage High Speed Charge Pump design
  Charge Pump Design 5: Charge Pump Design for Ultra Low Power PLL
  Charge Pump Design 6: Charge Pump Design for Low Phase Noise Low Power PLL
  Charge Pump Design 7: A Fully Differential Charge Pump
  Charge Pump Design 8: Charge Pump Design for a Low Power PLL
Summary
Reference

## Slide 45: CHARGE PUMP DESIGN 8 [13]
This paper proposes a low power PLL
The charge pump circuit used is as shown in
fig 24.
The buffering before the UP and DN pulses arrive
in the charge pump is to reduce dead zone. ???
Result
Total Power (1.5 GHz) 318.12 µW
CP Power (1.5 GHz) 183 µW
Fig 24a. Schematic of the charge pump for the design [13]
Fig 24b. Power break down of the PLL [13]

## Slide 46: OUTLINE
Introduction
The Charge Pump
Basic Principle of Operation of a Conventional Charge Pump
Non-ideal Behavior
  Charge Sharing
  Charge Injection and Clock Feedthrough
  Current Mismatch
Charge pump architectures
  Type 1: Conventional Tristate
  Type 2: Current Steering Topology
  Type 3: Differential Input with Single – Ended Output Topology
  Type 4: Fully Differential Charge Pump Topology
  Type 5: High Voltage Charge Pumps
Design Considerations
Typical Charge Pump Designs
  Charge Pump Design 1: Dual Compensation Charge Pump
  Charge Pump Design 2: NMOS Topology for a Dual Compensation Charge Pump Implementation
  Charge Pump Design 3: Dual Compension Implementation of a PMOS – NMOS Charge Pump Topology
  Charge Pump Design 4: Low Voltage High Speed Charge Pump design
  Charge Pump Design 5: Charge Pump Design for Ultra Low Power PLL
  Charge Pump Design 6: Charge Pump Design for Low Phase Noise Low Power PLL
  Charge Pump Design 7: A Fully Differential Charge Pump
  Charge Pump Design 8: Charge Pump Design for a Low Power PLL
Summary
Reference

## Slide 47: SUMMARY
Table 3: summary of the metrics of interest
Table 4: Summary of results

## Slide 48: OUTLINE
Introduction
The Charge Pump
Basic Principle of Operation of a Conventional Charge Pump
Non-ideal Behavior
  Charge Sharing
  Charge Injection and Clock Feedthrough
  Current Mismatch
Charge pump architectures
  Type 1: Conventional Tristate
  Type 2: Current Steering Topology
  Type 3: Differential Input with Single – Ended Output Topology
  Type 4: Fully Differential Charge Pump Topology
  Type 5: High Voltage Charge Pumps
Design Considerations
Typical Charge Pump Designs
  Charge Pump Design 1: Dual Compensation Charge Pump
  Charge Pump Design 2: NMOS Topology for a Dual Compensation Charge Pump Implementation
  Charge Pump Design 3: Dual Compension Implementation of a PMOS – NMOS Charge Pump Topology
  Charge Pump Design 4: Low Voltage High Speed Charge Pump design
  Charge Pump Design 5: Charge Pump Design for Ultra Low Power PLL
  Charge Pump Design 6: Charge Pump Design for Low Phase Noise Low Power PLL
  Charge Pump Design 7: A Fully Differential Charge Pump
  Charge Pump Design 8: Charge Pump Design for a Low Power PLL
Summary
Reference

## Slide 49: REFERENCE
[1] Woogeun Rhee, “Design of High – Performance CMOS Charge Pumps in Phase – locked loops.”
[2] Dong – Keon Lee, Jeong – Kwang Lee, and Hang – Geun Jeong, “A Dual – Compensated Charge Pump with Reduced Current Mismatch”
[3] M.-S. Hwang, J. Kim and D.-K. Jeong, “Reduction of pump current mismatch in charge-pump PLL” http://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=4770439
[4] Jae Hyung Noh, and Hang Geun Jeong, “Charge-Pump with a Regulated Cascode Circuit for Reducing Current Mismatch in PLLs”
[5] Hong Yut, Yasuaki Inouet, and Yan Han, “A New High-Speed Low-Voltage Charge Pump for PLL Applications” http://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=1611344
[6] Kyung-Soo Ha and Lee-Sup Kim, “Charge-Pump reducing current mismatch in DLLs and PLLs” http://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=1693061
[7] Shanfeng Cheng, Haitao Tong, Jose Silva-Martinez, and Aydin Ilker Karsilayan, “Design and Analysis of an Ultrahigh-Speed Glitch-Free Fully Differential Charge Pump With Minimum Output Current Variation and Accurate Matching”
[8] Jean-François Richard and Yvon Savaria, “High Voltage Charge Pump Using Standard CMOS Technology”
[9] Janusz A. Starzyk, Ying-Wei Jan, and Fengjing Qiu, “A DC–DC Charge Pump Design Based on Voltage Doublers”
[10] Nick Van Helleputte and Georges Gielen “An Ultra-low-Power Quadrature PLL in 130nm CMOS for Impulse Radio Receivers” http://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=4463309&tag=1
[11] Q. Guo, H. F. Zhou, W. W. Cheng, Y. Han, X. X. Han, and X. Liang, “A Low Phase-noise Low-power PLL in 0.13-¹m CMOS for Low Voltage Application”
[12] Gong Zhichao, Lu Lei, Liao Youchun, and Tang Zhangwen, “Design and noise analysis of a fully-differential charge pump for phase-locked loops”
[13] Po-Yao Ke and Jon Guerber, “A 1.3V Low Power Divide by 4 PLL Design with Output Range 0.5GHz-1.5 GHz”
[14] Partha Pratim Ghosh, “ Design and Study of Phase Locked Loop for Space Applications In Submicron CMOS Technology”
BOOKS:
    Low – Voltage CMOS RF Frequency Synthesizers by Howard C. Luong and Gerry C. T. Leung
    High Speed CMOS Circuits for Optical Receivers by Jafar Savoj and Behzad Razavi